## Slide 1
Verilog Review and Advance
Speaker: Fu-Sheng Yu (于富昇)

## Slide 2
Outline
Design flow overview
Verilog basic introduction
Hardware advance topic

## Slide 3
HDL vs Software Language

## Slide 4
Cell-Based IC Design
Specifications
RTL Coding
Synthesis
DFT Insertion
Place and Route
Tape Out
ATPG
DRC LVS
Front-End
Back-End
Test Patterns
Layout
RTL code
Gate-level netlist
GDS Layout

## Slide 5
Circuit Abstraction

## Slide 6
RTL simulation
Testbed.v
Design.v

## Slide 7
Common issues
ncverilog testbed.v design.v +access+r to dump waveform
+notimingcheck if using SRAM
$fsdbDumpvars(0,"+mda") to dump all memory signal, including 2D array

## Slide 8
Synthesis
Map your RTL code to standard cell
Optimization to meet timing constraint
Static timing analysis (STA)

## Slide 9
RTL vs Gate-Level
RTL
Gate-level
1
0
in2
in1
out
sel

## Slide 10
Gate-level simulation
Use the same pattern in RTL simulation
Dynamic timing analysis (DTA)

## Slide 11
Outline
Design flow overview
Verilog basic introduction
Hardware advance topic

## Slide 12
Combinational & Sequential
1
0
sel
in2
clk
in1
clk
clk
Combinational Part
Sequential Part
Memory-less
Always running
out

## Slide 13
Sequential Part
Describe the behavior of sequential circuit
always @ ( <sensitivity edge > <clock> [or <sensitivity edge> < reset >] )
if ( reset ) … ; // reset mode
else … ; // normal mode
Asynchronous reset Synchronous reset
D Q
rst
clk
count
next_count

## Slide 14
Asynchronous & synchronous reset
Asyn
reset
Syn
reset
Syn
reset
reset at the posedge of reset signal
reset at the posedge of clock signal
no reset occurs

## Slide 15
Metastability
The unstable status due to non ideal data transition is called metastability.

## Slide 16
Setup time & Hold time
Setup time( : the minimum amount of time the data signal should be held steady before the clock.
Hold time ( : the minimum amount of time the data signal should be held steady after the clock

## Slide 17
Critical Path
Delay: 5ns
clk
clk
Delay: 3ns
clk
Critical path is the path that has longest delay between reg or in/out in the whole circuit.

## Slide 18
Pipeline
Delay: 4ns
clk
Delay: 4ns
clk
Delay: 4ns
clk
clk
Delay: 4ns
clk

## Slide 19
Input buffer
Input Delay
4ns
Delay: 4ns
clk
Input Delay
4ns
Delay: 4ns
clk
clk

## Slide 20
Clear control
Controlling Unit
Processing Unit
Circuit

## Slide 21
Finite State Machine (FSM)
IDLE
DOWN
ZERO
down =1
count=0

## Slide 22
Behavior Modeling of FSM
Combinational Part
  Next-state logic (NL)
  Output logic (OL)
Sequential Part
  Current state (CS) stored in flip-flops
3 Coding Style
  Separate CS, OL and NL
  Combine NL+ OL, separate CS
  Combine CS + NL, separate OL

## Slide 23
Coding Style 1: Separate CS, OL and NL

## Slide 24
Code Sample of FSM

## Slide 25
Code Sample of FSM

## Slide 26
Finite State Machine (FSM)

## Slide 27
Common issues
Data type “reg” is NOT definitely to be a register. Instead, the synthesis result depends on the described behavior of RTL.
Multiple Driven Signals issue
  The variable of data type “wire” can NOT be repeatedly assigned.
  The variable of data type “reg” can only be assigned in single always block.
x
x

## Slide 28
Common issues
Avoid appearance of Latch during synthesis.
  Latch is too advanced for beginner of digital circuit.
  Latch is due to incomplete assignment in combinational part.
  Incomplete assignment implies that circuit will hold the previous
Usage of positive & negative clock simultaneously is NOT recommended.
  Timing issue will cause the poor performance if not design properly.
  Complicated clock tree for skew issue during place and route.

## Slide 29
Outline
Design flow overview
Verilog basic introduction
Hardware advance topic
  Design ware
  Memory
  System verilog

## Slide 30
Design ware
IP(Intellectual Property)
  Hard IP: GDSII format
  Firm IP: Netlist resource
  Soft IP: RTL design
In Media 11
  Datasheet and manual are in /opt/CAD/synopsys/synthesis/2019.12/dw/doc/

## Slide 31
Design ware
RTL behavior simulation
  Absolute path:
    `include “/opt/CAD/synopsys/synthesis/2019.12/dw/sim_ver/DW_sqrt.v"
  Relative path:
    `include "DW_sqrt.v“
    ncverilog tb.v design.v -incdir /opt/CAD/synopsys/synthesis/2019.12/dw/sim_ver/
Synthesis
Usage

## Slide 32
Memory

## Slide 33
SRAM
Slower but has less area than register
Only one address can be accessed in same time(single port SRAM)

## Slide 34
DRAM
Off chip memory, Read/Write latency penalty is huge
Data burst

## Slide 35
SystemVerilog - Logic data type
Reason: The datatype isn’t equal to the real circuit.
    reg doesn’t mean a register. It depends on how you use these variables.
So, in SystemVerilog, a new type “logic” is introduced to replace both of them.
    reg
        for procedural assignment (within always block)
        Flip-Flop must be the data type of “reg”
    wire
        for continuous assignment (assign)
module MyModule( input wire a, output reg b, input wire c, output wire d,
module MyModule( input logic a, output logic b, input logic c, output logic d,

## Slide 36
SystemVerilog - always blocks
Replace all always@(*) by always_comb
Replace sequential always block by always_ff

## Slide 37
SystemVerilog - Enum & unique case

## Slide 38
SystemVerilog - type define

## Slide 39
Reference
Slide from Hung-Chang Lu
Slide from Shao-Syuan Huang
Slide from NTU CVSD course
Slide from NCTU ICLAB course