## Slide 1: Verilog Coding Guidelines
Digital Circuit Lab
TA: Po-Chen Wu

## Slide 2: Outline
Introduction to Verilog HDL
Verilog Syntax
Combinational and Sequential Logics
Module Hierarchy
Write Your Design
Finite State Machine

## Slide 3: Introduction to Verilog HDL

## Slide 4: What is Verilog Doing…
+
-
MUX
Abs
DFF
Wafer
Chip
Module
Standard Cell
Layout
Verilog
Backend
EDA Tools
Logic

## Slide 5: Verilog HDL
Verilog HDL
  Hardware Description Language
  Programming language
  Describes a hardware design
Other hardware description language
  VHDL

## Slide 6: Represent a Circuit (1/2)
In software
  max_abcd = max( max(a,b), max(c,d) );
In verilog ??
max
max
max
a
b
c
d
max_abcd
max_ab
max_cd

## Slide 7: Represent a Circuit (2/2)
max
max
max
a
b
c
d
max_abcd
max_ab
max_cd
wire [3:0] a, b, c, d;
reg [3:0] max_ab; max_cd;
reg [3:0] max_abcd;
always@(*) begin
max_ab = (a > b)? a: b;
max_cd = (c > d)? c: d;
max_abcd = (max_ab > max_cd)? max_ab: max_cd;
end
data declaration
logic behavior

## Slide 8: Verilog Syntax

## Slide 9: Blocking and Nonblocking Statements (1/2)
Blocking Statements "="
  A blocking statement must be executed before the execution of the statements that follow it in a sequential block.
Nonblocking Statements "<="
  Nonblocking statements allow you to schedule assignments without blocking the procedural flow.

## Slide 10: Blocking and Nonblocking Statements (2/2)
module block_nonblock();
reg a, b, c, d, e, f;
// Blocking assignments
initial begin
a = #10 1'b1; // The simulator assigns 1 to a at time 10
b = #20 1'b0; // The simulator assigns 0 to b at time 30
c = #40 1'b1; // The simulator assigns 1 to c at time 70
end
// Nonblocking assignments
initial begin
d <= #10 1'b1; // The simulator assigns 1 to d at time 10
e <= #20 1'b0; // The simulator assigns 0 to e at time 20
f <= #40 1'b1; // The simulator assigns 1 to f at time 40
end
endmodule

## Slide 11: Data Types (1/3)
wire
  Used as inputs and outputs within an actual module declaration.
  Must be driven by something, and cannot store a value without being driven.
  Cannot be used as the left-hand side of an = or <= sign in an always@ block.
  The only legal type on the left-hand side of an assign statement.
  Only be used to model combinational logic.

## Slide 12: Data Types (2/3)
reg
  Can be connected to the input port (but not output port) of a module instantiation.
  Can be used as outputs (but not input) within an actual module declaration.
  The only legal type on the left-hand side of an always@ (or initial) block = or <= sign.
  Can be used to create registers when used in conjunction with always@(posedge Clock) blocks.
  Can be used to create both combinational and sequential logic.

## Slide 13: Data Types (3/3)
wire [15:0] longdata; // 16-bit wire
wire shortvalue; // 1-bit wire
reg [3:0] areg; //4-bit reg
assign longdata = areg + 88;
always@(*) begin
if(shortvalue == 1'b1)
areg = shortvalue + 3;
else
areg = shortvalue + 7;
end
logic behavior
data declaration
wire
reg

## Slide 14: Value Set
0 - logic zero, or false condition
1 - logic one, or true condition
z - high-impedance state
x - unknown logic value – unrealistic value in design
0
logic low
1
logic high
z
high-impedance
x
unknown

## Slide 15: Numbers
binary('b), decimal('d), hexadecimal('h), octal('o)
Format
  <number>: reg data = 127;
  '<base><number>: reg data = 'd127;
  <width>'<base><number> → complete format
reg data =
659 // decimal
'o7460 // octal
4'b1001 // 4-bit binary
3'b01x // 3-bit with unknown
16'hz // 16-bit high impedance
-8'd6 // two’s complement of 6
8'd-6 // illegal syntax
4af // illegal (requires 'h)

## Slide 16: Case-Sensitive Control
Suspends subsequent statement execution until any of the specified list of events occurs
  Support event driven simulation
Sensitivity list
  always@(… or … or … or…)
  always@(a or b or c )
  always@(*)
    verilog 2001, automatic list generation

## Slide 17: Operators (1/6)
Arithmetic operators
  +, -, *, /, %
Bitwise operators
  Perform the operation one bit of a operand and its equivalent bit on the other operand to calculate one bit for the result
  ~, &, |, ^, ~^
Arithmetic operators
Bitwise operators

## Slide 18: Operators (2/6)
Unary reduction operators
  Perform the operation on each bit of the operand and get a one-bit result
  &, ~&, |, ~|, ^, ~^
Unary reduction operators
^4’b11110
^4’b11101
|4’b00000
|4’b00011
&4’b11100
&4’b11111
Unary reduction AND
Unary reduction OR
Unary reduction XOR

## Slide 19: Operators (3/6)
Logical operators operate with logic values
  Equality operators
    Logical equality
    ==, !=
    Case equality
    ===, !==
Logical negation
  !
Logical
  &&, ||
Logical operators
!4’b0100  0
!4’b0000  1
!4’b00z0  x
example

## Slide 20: Operators (4/6)

## Slide 21: Operators (5/6)
Concatenation operator
  {}
  Join bits from two or more
  expressions together
  Very convenient
  Multiple layers
  {{},{}…}
Replication operator
  {n{}}
a
b
c
d
y
y = {a[1:0], b[2], c[4,3], d[7:5]}
y
a
y = {{4{a[3]}},a}

## Slide 22: Operators (6/6)
Shift operators
  <<, >>
Relational operators
  <, <=, >=, >
Conditional operator
  ? :
if(a <= b) d = 0;
else d = 1;
d = (a<=b) ? 0 : 1
Operator precedence

## Slide 23: Combinational and Sequential Logics

## Slide 24: Two Types of Logics (1/2)
Combinational Logics
  data-in → data-out
  instant response
  fixed arrangement
max
max
max
a
b
c
d
max_abcd
max_ab
max_cd

## Slide 25: Two Types of Logics (2/2)
Sequential Logics
  always and only update at
  clock edges
  posedge / negedge
  memory
1 cycle
clk
a
a_d1
a_d2
a_d3
D Q
clk
D Q
clk
D Q
clk

## Slide 26: Case-Sensitive Control (1/2)
register in sequential changes only at clock edges
with reset signal
always@(posedge clk) begin
……
end
always@(negedge clk) begin
……
end
always @(posedge clk or negedge rst_n) begin
......
end

## Slide 27: Case-Sensitive Control (2/2)
Sequential Logics
  always and only update at clock edges
  posedge / negedge
reg [3:0] a, b; // declaration
always @(posedge clk or negedge rst_n) begin
if(rst_n ==1'b0) begin //registers
a <= 4'd0;
b <= 4'd0;
end
else begin
a <= next_a;
b <= next_b;
end

## Slide 28: The Use of Sequential Circuits?
Temporal storage (memory)
Split long computation lines
  timing issue
  divide circuits into independent stages
    work at the same time !!
Combinational logics handle the computation
Sequential logics store inter-stage temporal data

## Slide 29: Sequential and Combinational Logics
always @(posedge clk) begin
if(~rst_n) begin
a <= 3'd0;
end
else begin
a <= next_a;
end
assign c = b [2:0];
assign d = c & 3'b101;
always@(a or d) begin
sum = a + d;
......
end
Sequential Logic
(Register)
Combinational
Logic
Combinational
Logic
Sequential Logic
(Register)
Sequential Logic
(Register)
clk

## Slide 30: Sequential Circuit (1/3)
Synchronous reset
always @(posedge clk) begin
if(~rst_n) begin
a <= 8'd0;
end
else begin
a <= next_a;
end
clk
rst_n
next_a
a
8'h01
XX
8'h5a
8’h00
8’h01
8’h5a

## Slide 31: Sequential Circuit (2/3)
Asynchronous reset
always @(posedge clk or negedge rst_n) begin
if(~rst_n) begin
a <= 8'd0;
end
else begin
a <= next_a;
end
clk
rst_n
next_a
a
8'h01
XX
8'h5a
8’h00
8’h01
8’h5a

## Slide 32: Sequential Circuit (3/3)
Synchronous reset | Pros | Easy to synthesize, just another synchronous input to the design
 | Cons | Require a free-running clock, especially at power-up, for reset to occur
Asynchronous reset | Pros | Does not require a free-running clock Uses separate input on FF, so it does not affect FF data timing
 | Cons | Harder to implement, usually a tree of buffers is inserted at P&R Makes static timing analysis and cycle-based simulation more difficult, and can make the automatic insertion of test structures more difficult
Prefer

## Slide 33: Module Hierarchy

## Slide 34: What is a Module?
Group circuits into meaningful building blocks
Combine highly-related circuits
Leave simple i/o interface
Easier to reuse / maintain
+
-
MUX
DFF
Abs
Module

## Slide 35: A Module
module maxab(clk,rst_n,a,b,maxab);
input clk;
input rst_n;
input [3:0] a;
input [3:0] b;
output [3:0] maxab;
reg [3:0] maxab;
wire [3:0] next_maxab;
assign next_maxab = (a>b)? a: b;
always@(posedge clk or negedge rst_n) begin
if (rst_n == 1'b0) begin
maxab <= 4'd0;
end
else begin
maxab <= next_maxab;
end
end
endmodule
module port definition
wire, reg declaration
combinational logics
sequential logics
ending your module!
max
clk
a
b
maxab
rst_n
D Q
rst_n
clk

## Slide 36: Connection Between Modules (1/2)
Where you "cut" your design.
max
max
max
a
b
c
d
maxabcd
D Q
clk
D Q
clk
D Q
clk

## Slide 37: Connection Between Modules (2/2)
Where you "cut" your design.
max
max
max
a
b
c
d
maxabcd
maxab
maxcd
D Q
clk
D Q
clk
D Q
clk

## Slide 38: Module Instantiation
Build a module by smaller modules
module maxabcd(clk,rst_n,a,b,c,d,maxabcd);
input clk;
input rst_n;
input [3:0] a, b, c, d;
output [3:0] maxabcd;
wire [3:0] maxab, maxcd;
maxab m1(.clk(clk), .rst_n(rst_n), .a(a), .b(b), .maxab(maxab));
maxab m2(.clk(clk), .rst_n(rst_n), .a(c), .b(d), .maxab(maxcd));
maxab m3(.clk(clk), .rst_n(rst_n), .a(maxab), .b(maxcd), .maxab(maxabcd));
endmodule
a
b
maxabcd
max
max
max
c
d
maxab
maxcd
DQ
clk
DQ
clk
DQ
clk

## Slide 39: Write Your Design

## Slide 40: Use Parameters (1/2)
Build a module by smaller modules
`define INST_WakeUp 0
`define INST_GoToSleep 1
`define BUS_WIDTH 64
input [`BUS_WIDTH-1:0] databus;
case (instruction)
`INST_WakeUp:
…
`INST_GoToSleep:
…
endcase

## Slide 41: Use Parameters (2/2)
Use parameter for reusable modules
Use localparam for inner-module variables
parameter [4:0] FA_BitSize = 8;
reg [FA_BitSize-1:0] = datain;
localparam FSM_StateSize = 5;
localparam [FSM_StateSize-1:0] FSM_Idle = 5'd0;

## Slide 42: Finite State Machine

## Slide 43: Finite State Machine (1/2)
Synchronous (i.e. clocked) finite state machines (FSMs) have widespread application in digital systems
  Controllers in computational units and processors.
Synchronous FSMs are characterized by
  A finite number of states
  Clock-driven state transitions.

## Slide 44: Finite State Machine (2/2)

## Slide 45: Elements of FSM (1/2)
Memory elements (ME)
  Memorize current state (CS)
  Usually consist of FF or latch
  N-bit FF have 2N possible states
Next-state logic (NL)
  Combinational logic
  Produce next state
  Based on current state (CS) and input (X)

## Slide 46: Elements of FSM (2/2)
Output logic (OL)
  Combinational logic
  Produce outputs (Z)
  Based on current state (Moore)
  Based on current state and input (Mealy)

## Slide 47: Moore Machine
Output is function of CS only
  Not function of inputs
Next-state Logic
(NL)
Memory
Element
(ME)
Output
Logic
(OL)
Next
State
(NS)
Current
State
(CS)
Input
X
Output
X

## Slide 48: Mealy Machine
Output is function of both
  Input and current state
Next-state Logic
(NL)
Memory
Element
(ME)
Output
Logic
(OL)
Next
State
(NS)
Current
State
(CS)
Input
X
Output
X

## Slide 49: Modeling FSM in Verilog
Sequential circuits
  Memory elements of current state (CS)
Combinational circuits
  Next-state logic (NL)
  Output logic (OL)

## Slide 50: The End.
Any question?

## Slide 51: Reference
"Verilog_Coding_Guideline_Basic" by members of DSP/IC Design Lab
http://inst.eecs.berkeley.edu/~cs150/Documents/Nets.pdf by Chris Fletcher, UC Berkeley
CIC training course： "Verilog_9807.pdf"
http://www.asic-world.com/