## Slide 1: Introduction to Kalman Filter
Po-Chen Wu
Media IC and System Lab
Graduate Institute of Electronics Engineering
National Taiwan University

## Slide 2: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 3: Takeaways
What is a Kalman Filter?
Why do we need Kalman Filters?

## Slide 4: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 5: Introduction
Recursive data processing algorithm
  Generates optimal estimate of desired quantities given the set of measurements
  Optimal: For linear system and white Gaussian errors, Kalman filter is “best” estimate based on all previous measurements.
  Recursive: doesn’t need to store all previous measurements and reprocess all data each time step.

## Slide 6: The Problem
System state cannot be measured directly.
Need to estimate “optimally” from measurements.
Measuring Devices
Estimator
Measurement
Error Sources
System State (desired but not known)
External Controls
Observed Measurements
Optimal Estimate of System State
System
Error Sources
System
Black Box

## Slide 7: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 8: Conceptual Overview (1/9)
Lost on the 1-dimensional line
Position –
Assume Gaussian distributed measurements

## Slide 9: Conceptual Overview (2/9)
Sextant Measurement at : Mean = and Variance =
Optimal estimate of position is:
Variance of error in estimate:
Boat in same position at time - Predicted position is

## Slide 10: Conceptual Overview (3/9)
So we have the prediction
GPS Measurement at : Mean = and Variance =
Need to correct the prediction due to measurement to get
Closer to more trusted measurement – linear interpolation?
prediction
measurement

## Slide 11: Conceptual Overview (4/9)
Corrected mean is the new optimal estimate of position
New variance is smaller than either of the previous two variances
corrected optimal estimate
prediction
measurement

## Slide 12: Conceptual Overview (5/9)
Lessons so far:
Make prediction based on previous data: ,
Take measurement: ,
Optimal estimate () = Prediction + (Kalman Gain) * (Measurement - Prediction)
Variance of estimate = Variance of prediction * (1 – Kalman Gain)

## Slide 13: Conceptual Overview (6/9)
At time , boat moves with velocity
Naïve approach: Shift probability to the right to predict
This would work if we knew the velocity exactly (perfect model)
Naïve Prediction

## Slide 14: Conceptual Overview (7/9)
Better to assume imperfect model by adding Gaussian noise
Distribution for prediction moves and spreads out
Prediction
Naïve Prediction

## Slide 15: Conceptual Overview (8/9)
Now we take a measurement at
Need to once again correct the prediction
Same as before
Corrected optimal estimate
Measurement
Prediction

## Slide 16: Conceptual Overview (9/9)
Lessons learnt from conceptual overview:
  Initial conditions ( and )
  Prediction ( , )
    Use initial conditions and model (eg. constant velocity) to make prediction
  Measurement ()
    Take measurement
  Correction ( , )
    Use measurement to correct prediction by ‘blending’ prediction and residual – always a case of merging only two Gaussians
    Optimal estimate with smaller variance

## Slide 17: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 18: Theoretical Basis
Process to be estimated:
Kalman Filter
Process Noise () with covariance
Measurement Noise () with covariance
Predicted: is estimate based on measurements at previous time-steps
Corrected: has additional information – the measurement at time
Optimal Kalman gain
Predicted (a priori) state estimate
Predicted (a priori) estimate covariance

## Slide 19: Blending Factor
If we are sure about measurements:
  Measurement error covariance () decreases to zero
  increases and weights residual more heavily than prediction
If we are sure about prediction
  Prediction error covariance decreases to zero
  decreases and weights prediction more heavily than residual

## Slide 20: Theoretical Basis
Prediction (Time Update)
(1) Project the state ahead
(2) Project the error covariance ahead
Correction (Measurement Update)
(1) Compute the Kalman Gain
(2) Update estimate with measurement zk
(3) Update Error Covariance
Initial estimates for and

## Slide 21: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 22: Simple Example (1/4)
Consider a truck on perfectly frictionless, infinitely long straight roads.
  Initially the truck is stationary at position 0, but it is buffeted this way and that by random acceleration.
  We measure the position of the truck every Δt seconds, but these measurements are imprecise; we want to maintain a model of where the truck is and what its velocity is.
  We show here how we derive the model from which we create our Kalman filter.
x

## Slide 23: Simple Example (2/4)
The position and velocity of the truck are described by the linear state space:
We assume that between the (k−1) and k timestep the truck undergoes a constant acceleration of ak that is normally distributed, with mean 0 and standard deviation σa.
,

## Slide 24: Simple Example (3/4)
At each time step, a noisy measurement of the true position of the truck is made.
Let us suppose the measurement noise is also normally distributed, with mean 0 and standard deviation σz.

## Slide 25: Simple Example (4/4)
We know the initial starting state of the truck with perfect precision, so we initialize
And to tell the filter that we know the exact position, we give it a zero covariance matrix:
If the initial position and velocity are not known perfectly the covariance matrix should be initialized with a suitably large number, say L, on its diagonal.
( )

## Slide 26: Outline
Introduction to Kalman Filter
Conceptual Overview
The Theory of Kalman Filter
Simple Example
Extended Kalman Filter

## Slide 27: Extended Kalman Filter
The basic Kalman filter is limited to a linear assumption.
The extended Kalman filter (EKF) is the nonlinear version of the Kalman filter which linearizes about an estimate of the current mean and covariance.

## Slide 28: Theoretical Basis
Prediction (Time Update)
(1) Project the state ahead
(2) Project the error covariance ahead
Correction (Measurement Update)
(1) Compute the Kalman Gain
(2) Update estimate with measurement zk
(3) Update Error Covariance
Initial estimates for and

## Slide 29: Reference
Bishop, Gary, and Greg Welch. "An introduction to the Kalman filter." Proc of SIGGRAPH, Course 8.27599-23175 (2001): 41.
Michael Williams. "Introduction to Kalman Filters." Powerpoint Slides, 5 June 2003